## Slide 1: Improving urban flood detection Project Update
Katy Sill
April 9, 2019

## Slide 2: Our urban world
By 2005, the urban population is expected to grow by 2.5 billion people
90% of this growth is predicted to take place in Africa and Asia
With climate change, more extreme events expected, including floods

## Slide 3: Cloud to Street
High-resolution maps of flood-prone areas for:
  planners
  insurers
  disaster response agencies..
To better:
  prepare for floods
  respond to flood events in near real-time
  understand and price flood risk
  insure vulnerable populations
Notes: Millions of people in cities are affected by flooding events each year. Cloud to Street, my partner for this project, uses satellite imagery to make high resolution maps for flood prone areas in low and middle income countries. These maps are designed to enable decision makers the best information possible to prepare and respond to flooding events, to better understand and price flood risk

## Slide 4: Urban flood map challenges
NDWI does not work well in urban settings due to interferences from the built environment
High resolution imagery does not include the required SWIR band to calculate MNDWI
Attempts at using a combination of indices and bands may fall short of mapping the true flooding extent
Building shadows look visually similar to flood waters and can be misidentified

## Slide 5: Current flood map issues
Areas of flood not captured by flood map
Building shadow misidentified as flood
WorldView-2
Cloud to Street Flood Map

## Slide 6: Project goals
Improve flood detection workflow
Focused on differentiating building shadow and flood waters
Explore open source Python-based tools
Cloud to Street uses Google Earth Engine and is interested in exploring other options
Geographic focus
Abidjan, Ivory Coast
Flooding event from June 2016
Final products
A report of the different potential options explored for improving the workflow
A final workflow to create an improved flood extent map for Abidjan (and potentially other cities*)
Academic paper (?)

## Slide 7
Flood Detection Project Approach
Create reference dataset
60% for model development
40% for model validation
Threshold spectral and morphological indices
Develop unsupervised machine learning model
Kmeans
Gaussian mixture model
Train/test supervised machine learning model
- Support Vector Machine
Compare outputs to reference dataset
Validate final models using validation dataset
Analyze final model outputs
Write analysis report
Select model and finalize proposed workflow
Explore imagery and
select area of interest
Calculate spectral and
morphological indices
Iterate to improve models where possible
Notes: This is an overview of the steps needed to complete this project. The orange boxes are tasks I have completed, the yellow is where I am at currently and the green are things I still need to do. Briefly, what I’ve done so far is to explore the flooded image and identified a representative sub-section of the city to focus my analysis. I then started by trying to recreate and improve the algorithm using a similar approach as cloud to street, so basically combining and thresholding spectral indices, adding in new measures which help identify shadow and building footprints. The result so far is mixed.. There is definitely a benefit by adding in shadow – but otherwise it is a bit mixed. I then looked at supervised and unsupervised machine learning models. For supervised I looked support vector machine, or SVM and for unsupervised I have looked at both Kmeans and the Gaussian mixture model, with most of my efforts on kmeans. For SVM, I needed to develop a reference data set for training and testing the model, so I used ArcGIS to drop points on specific areas of the image that identified flood, shadow and other land cover types. So right now I am analyzing the outputs of these three approaches and seeing if I can iterate to make any improvements to the model. Next steps are to validate the final model and

## Slide 8: Validation Process
For the development of the SVM map, the reference data set was divided:
  60% for training and testing
    40% for testing
    60% for training
  40% for external validation
  SVM map was created based the entire image
The Kmeans and thresholding maps were created based on the entire image.
  Accuracy scores were calculated for the 60% training/testing dataset, the 40% external dataset and the entire reference dataset.

## Slide 9: Cloud to Street Abidjan Map
Include algorithm

## Slide 10: Cloud to Street – All Reference Data (shadow, flood, other)
Accuracy score (all data) = 32%
Accuracy score (60%) = 32%
Accuracy score (40%) = 32%

## Slide 11: Cloud to Street – Flood Only (flood, other)
Accuracy score (all data) = 33%
Accuracy score (60%) = 35%
Accuracy score (40%) = 31%

## Slide 12: (Delete) Thresholding Result
Appears to miss substantial amount of flooding
Shadows reasonably well represented
Challenges/Next steps
Re-examine and finalize thresholds
Calculate accuracy score and confusion matrix

## Slide 13: New Thresholding Result
Changed representation of flood from Cloud to Street algorithm to just NDWI calculated using yellow_band and near_ir2 (NDWI2)
Increased threshold to
> -0.12
Much improves visualization and accuracy score
ADD LEGEND

## Slide 14: Thresholding Challenges/Questions
Explore if MBI can be further improved.. Does not currently appears to add much value.. Still significant building/flood confusion.
Ask Jeff more about the existence of building footprint layers, etc.
Compare “Flood” vs. NDWI2 accuracy scores

## Slide 15: Threshold Map Accuracy Scores and Confusion Matrices
Accuracy score (60%) = 62%
Accuracy score (all data) = 61%
Accuracy score (40%) = 60%

## Slide 16: Support Vector Machine (SVM)
Challenges/Next steps:
- Make an SVM-based flood map to better
visualize model results
- Conduct sensitivity analysis to
determine ideal model inputs
Training data to develop model
Test data to internally validate model
External data to fully validate model
Current 5 inputs include:
- Dark parameter (sum of RE and NIR1&2)
- NDWI – MSI (x2)
- MBI
- MSI
Internal testing accuracy score:
96%
External validation accuracy score:
90%
Confusion Matrix
Validated model
60% of reference points
40% of reference points

## Slide 17: SVM Sensitivity Analysis
Parameters Included | Accuracy Scores (%) | 
 | 40% Reference Data (test) | 40% external data
Dark, MBI, MSI, NDWI_coastal – MSI, NDWI_green – MSI | 95.9 | 90.6
Dark, MBI, MSI,NDWI_green, NDWI_yellow, NDWI_coastal – MSI, NDWI_green – MSI, NDWI_yellow – MSI | 93.4 | 91.8

## Slide 18: New SVM Resulting Map
Blue – water
Pink – building shadow
Grey – other

## Slide 19: SVM Map Accuracy Scores and Confusion Matrices
Accuracy score (test data)= 95.9%
Accuracy score (external 40%) = 90.6%

## Slide 20: Random Forest Resulting Map
Blue – water
Pink – building shadow
Grey – other

## Slide 21: Random Forest Map Accuracy Scores and Confusion Matrices
Accuracy score (test data)= 93%
Accuracy score (external 40%) = 92.8%

## Slide 22: SVM Challenges/Questions
Explore other combinations for inclusion for the training dataset.
Consider adding NDWI2 (yellow/NIR2)
Document trials

## Slide 23: K-means Result
K-means appears to capture shape of floodwaters more accurately

## Slide 24: Water and shadow in overlapping clusters
K-means clusters Pink = shadows Blue = water Green = vegetation Grey = buildings
Reference points Pink = shadow Blue = water Green = other
Challenges/Next steps:
Try to refine clusters that include both shadow and water
Try to combine shadow index with K-means
Make sure k-means isn’t over-representing flood

## Slide 25: New k-means Result
Includes 8-band stack and shadow_mask
Shadow mask = MSI > 0.12, disk_size = 2
Continue to test accuracy scores on various kmeans efforts.

## Slide 26: k-means Map Accuracy Scores and Confusion Matrices
Accuracy score (60%) = 83%
Accuracy score (all data) = 84%
Accuracy score (40%) = 84%

## Slide 27: Labeled k-means
Final k-means geotiff was labeled using skimage.measure.label()
Region properties were then calculated using regionprops()
Result includes properties for each labeled region
Reviewed properties for clusters containing flood and shadow
  Using 60% reference point data set, explored characteristics and moved clusters based on thresholds
    Area
    Perimeter
    Etc.

## Slide 28: Labeled k-means Map Accuracy Scores and Confusion Matrices
Accuracy score (60%) = 79%
Accuracy score (all data) = 78%
Accuracy score (40%) = 78%
* Can increase accuracy score to ~83% by refining characteristics

## Slide 29: k-means Sensitivity Analysis
Kmeans | 40% accuracy | 100% accuracy
kmeans_all_bands | 82.8% | 82.5%
kmeans_cl_free | 82.8% | 82.5%
kmeans_shadow_free | 82.8% | 81.5%
kmeans_shadow_free_shadow_mask | 83.5% | 81.9%
kmeans_with_shadow_free_shadow_masked_texture | 82.4% | 81.0%
kmeans_with_shadow_build_mask | 81.8% | 80.9%
kmeans_cl_free_shadow_mask | 84.1% | 82.3%
kmeans_with_msi | 76.1% | 74.2%
kmeans_with_shadow_free_shadow_masked_texture | 82.4% | 81.0%
kmeans_cl_free_msi | 63.3% | 61.4%
kmeans_shadow_free_msi | 76.1% | 74.0%

## Slide 30: k-means Notes
Conducting sensitivity analysis to confirm which kmeans result appears best. Options include:
  Regular 8-band stack
  Cloud-masked 8-band stack
  Building Shadow, cloud-masked 8-band stack
  Shadow masked stack plus MSI 9-band stack
  Shadow masked stack plus smoothed MSI 9-band stack
  Shadow masked stack plus MSI shadow mask 9-band stack
  Shadow masked stack plus MSI shadow mask and MBI building mask 10-band stack
So far, most have similar accuracy scores. Including the shadow mask as a layer results in three clusters which include shadow and water, while using the 8-band stacks include only two clusters with water and shadow.
Will make table showing kmeans options with accuracy scores.
Rethink how data is being combined for accuracy score calculations. Currently matching based on label_ID but that results in reference points in the same label_ID region being lost.
  Appears to impact flood reference points more than shadow due to continuous nature of flood water labeled regions.
Currently exploring shape characteristics to see if clusters can be refined so that all shadow is in one cluster and all flood is in a separate cluster.
  Increased accuracy score of 60% reference dataset to 83%

## Slide 31: Challenges/Questions
Potential over-representation of flood waters??
  Kmeans
  SVM
  NDWI2 mask
Overlap between buildings and flood waters
  All maps
Could validation be done differently?
Is 1007 reference points enough?
  Should I even out the distribution of points?
    522 – shadow
    276 – water
    209 – other
Ask Jeff about more how Cloud to Street algorithms were finalized

## Slide 32: Remaining Tasks
Finalize models
Complete final model runs
Analyze validation and accuracy scores
Test model on other location*
Clean up code and finalize workflow
Write report of process and findings

## Slide 33: Future Work
Use Open Street Map building layer to more clearly delineate buildings from flood
  Currently limited buildings have been identified
  Proximity to building could help differentiate
  Shape/texture still worth exploring
Apply to entire image
  Expand training points to include more vegetation

## Slide 34: Steps needed
Cloud mask
Then shadow mask (?)
Can SVM accept shadow masked information?
Could always apply cloud mask afterwards?
Add slide with flood surface area calcs for each method

## Slide 35: Questions?
References:
  Huang, X., Xie, C., Fang, X., Zhang, L. (2015) Combining Pixel-and Object-Based Machine Learning for Identification of Water-Body Types from Urban High-Resolution Remote-Sensing Imagery. IEEE J. Sel. Top. Appl. Earth Obs. Remote Sens. 8, 2097–2110.
  Huang, X., and Zhang, L. (2012) Morphological Building/Shadow Index for Building Extraction From High-Resolution Imagery Over Urban Areas. IEEE J. Sel. Top. Appl. Earth Obs. Remote Sens. 5, 161-172.
  Xie, C., Huang, X., Zeng, W., & Fang, X. (2016). A novel water index for urban high-resolution eight-band WorldView-2 imagery. International Journal of Digital Earth, 9(10), 925–941.
  Cloud to Street. Urban Flood Mapping Using Very-High Resolution Satellite Imagery. Available at: https://abidjan.cloudtostreet.info/info
Acknowledgements:
  Jenny Palomino, CU Earth Lab
  Joe McGlinchy, CU Earth Lab
  Jeff Ho, Cloud to Street

## Slide 37: Combining Building Shadow Mask and K-means
Because MSI shadow mask appears to well capture building shadows, a combination of MSI with k-means could be interesting.
Trying to run kmeans on masked data
Apply shadow mask after the fact. Classify remaining clusters as flood, wet soil, etc?
Add MSI as an input for the kmeans calculations

## Slide 38: Abidjan, Cote D’Ivoire
5 million people
Francophone West Africa’s largest economy
21 people killed by flash flood in June 2018
X mm of rain fell
136 people rescued
Authorities intend to demolish structures and compensate owners
Notes: https://reliefweb.int/disaster/fl-2018-000077-civ

## Slide 39: Unique algorithms for each image

## Slide 40: Current flood map issues
Areas of flood not captured by flood map
Building shadow misidentified as flood
WorldView-2 RGB Image
Cloud to Street Flood Map